## Slide 1: Serial Communication
Kamalanath Samarakoon

## Slide 2: Characteristic Directions
Full duplex
Half duplex
Simplex

## Slide 3: Number of devices connected
Point to point
Multidrop

## Slide 4: Formats
Synchronous
Asynchronous

## Slide 5: Synchronous communication

## Slide 6: Asynchronous communication
1 8 N 1 = 8N1
Add parity for error detecting
1 7 E 1 = 7E1

## Slide 7: Signal
Single ended
Differential

## Slide 8: Line termination

## Slide 9: Serial communication protocols
Slow
  RS 232
  RS485
Fast
  USB
  I2C (IEEE 1384)
  FireWire

## Slide 10: RS232
Most popular interface before USB
Was available in almost all computer to mainframe
Advantages
  Was commonly available
  Can do that USB could not
  Less number of wires compared to parallel
  Inexpensive
  Very long cable (50 ft max)/USB 16ft // 10-15 ft
  3 wires to communicate (Unlike parallel)

## Slide 11: RS232
Disadvantages
  Cannot connect more than two devices
  Max speed 20,000 bits/s
  Very long lines need differential interface (RS485)

## Slide 12: RS232 Evolution
Originally
  PC to dumb terminal
Then
  PC to Internet
Also PC to
  Mouse
  Printer
  Another PC
  Microcontroller

## Slide 13: RS232
RS (Recommended Standard)
Standard is – EIA 232F (Electronic Industry Association)
This standard defines
  Names and functions of signals
  Electrical Characteristic of signals
  Mechanical standard (size, shape pin assignment)

## Slide 14: RS232
25 pins or 9 pins
Logic 0 +3 to +25 V
Logic 1 -3 to -25 V
- 3 to +3 V undefined
O/C V <25 V w.r.t to Ground
S/C I 500mA driver should be able to drive
Max speed 20,000 bps for 50 ft

## Slide 15: Connectors RS232 – 9 pin
Equipment
  Female
Cable
  Male

## Slide 17: Standard 9 to 25 pin cable layout for async data on a PC AT serial cable
Description | Signal | 9-pin DTE | 25-pin DCE | Source DTE or DCE
Carrier Detect | CD | 1 | 8 | from Modem
Receive Data | RD | 2 | 3 | from Modem
Transmit Data | TD | 3 | 2 | from Terminal/Computer
Data Terminal Ready | DTR | 4 | 20 | from Terminal/Computer
Signal Ground | SG | 5 | 7 | from Modem
Data Set Ready | DSR | 6 | 6 | from Modem
Request to Send | RTS | 7 | 4 | from Terminal/Computer
Clear to Send | CTS | 8 | 5 | from Modem
Ring Indicator | RI | 9 | 22 | from Modem

## Slide 18: Link
RJ Registered Jack of Universal service ordering code
RJ 11 6 points middle 2 connected
RJ 14 6 points middle 4 connected
RJ 25 6 points middle 6 connected
RJ 45 8 points

## Slide 19
Full Name | Function | 
TD | Transmit Data | Serial Data Output (TXD)
RD | Receive Data | Serial Data Input (RXD)
CTS | Clear to Send | This line indicates that the Modem is ready to exchange data.
DCD | Data Carrier Detect | When the modem detects a "Carrier" from the modem at the other end of the phone line, this Line becomes active.
DSR | Data Set Ready | This tells the UART that the modem is ready to establish a link.
DTR | Data Terminal Ready | This is the opposite to DSR. This tells the Modem that the UART is ready to link.
RTS | Request To Send | This line informs the Modem that the UART is ready to exchange data.
RI | Ring Indicator | Goes active when modem detects a ringing signal from the PSTN.

## Slide 20: Null Modem
XX

## Slide 21: No Handshake

## Slide 22: Full Handshake

## Slide 23: Loop back Handshake

## Slide 24: USART Universal Asynchronous Receiver/Transmitter
IC Module inside the IC for serial communication
Do parallel in PC to serial in RS232 conversion and back
Supports Half duplex and Full Duplex
Provide all standard RS232 handshaking and control lines

## Slide 25
8250 57600 bps
16450 115200 bps
16550 16 Bytes FIFO Buffers
16650 32 Byte FIFO Buffers
16750 64 Byte FIFO Buffers 230,400 bps

## Slide 26: Flow control
Program should set 115,200 kbps and not 33.6 kbps as DCE do compressing
DTE faster than DCE hence data can be lost
Hence use flow control

## Slide 27: Flow control
Software
Xoff – Xon
Hardware
  Use RTS and DTS lines

## Slide 28: Asynchronous communication
1 8 N 1 = 8N1
Add parity for error detecting
1 7 E 1 = 7E1

## Slide 29: References
Parallel port, Serial Port and USB
  beyondlogic.org
  http://retired.beyondlogic.org/spp/parallel.htm
Jan Axelson
  Parallel port complete
  Serial port complete
  USB complete

## Slide 30: Asynchronous serial communication by USART
UART uses clock that is 16 times bit frequency
E.g. 300 bps 4800 Hz
Detect start bit, wait 8, wait 16, read, wait 16, read…

## Slide 31: Calculation of bit rate
In PC UART cock rate is 1.8432 MHz
Calculate maximum bit rate

## Slide 32: Quiz
In PC UART cock rate is 1.8432 MHz
Calculate maximum bit rate
If bit rate is 9600bps
How many bytes it can transmit per second?
How many data bytes it can transmit per second when data format is 7E1?
960 bytes
1200 bytes

## Slide 33: 16550 UART
ur homemade devices and projects.

## Slide 34: Block diagram
PC Bus side
  Data lines
  Read and Write control
  Interrupt control
  Reset
  Address Lines
RS232 side
Clock

## Slide 35: UART

## Slide 37: Registers
Addresses = Base +7
12 registers some read and some write and R/W using DLAB (Devisor Latch Access Bit)

## Slide 38: Registers
Base Address | DLAB | Read/Write | Abr. | Register Name
+ 0 | =0 | Write | - | Transmitter Holding Buffer
 | =0 | Read | - | Receiver Buffer
 | =1 | Read/Write | - | Divisor Latch Low Byte
+ 1 | =0 | Read/Write | IER | Interrupt Enable Register
 | =1 | Read/Write | - | Divisor Latch High Byte
+ 2 | - | Read | IIR | Interrupt Identification Register
 | - | Write | FCR | FIFO Control Register
+ 3 | - | Read/Write | LCR | Line Control Register
+ 4 | - | Read/Write | MCR | Modem Control Register
+ 5 | - | Read | LSR | Line Status Register
+ 6 | - | Read | MSR | Modem Status Register
+ 7 | - | Read/Write | - | Scratch Register

## Slide 39: DLAByte
Speed (BPS) | Divisor (Dec) | Divisor Latch High Byte | Divisor Latch Low Byte | 
50 | 2304 | 09h | 00h | 
300 | 384 | 01h | 80h | 
600 | 192 | 00h | C0h | 
2400 | 48 | 00h | 30h | 
4800 | 24 | 00h | 18h | 
9600 | 12 | 00h | 0Ch | 
19200 | 6 | 00h | 06h | 
38400 | 3 | 00h | 03h | 
57600 | 2 | 00h | 02h | 
115200 | 1 | 00h | 01h | 

## Slide 40: LCR: Line Control Register
Bit 7 | 1 | Divisor Latch Access Bit |  |  | 
 | 0 | Access to Receiver buffer, Transmitter buffer & Interrupt Enable Register |  |  | 
Bit 6 | Set Break Enable |  |  |  | 
Bits 3, 4 And 5 | Bit 5 |  | Bit 4 | Bit 3 | Parity Select
 | X |  | X | 0 | No Parity
 | 0 |  | 0 | 1 | Odd Parity
 | 0 |  | 1 | 1 | Even Parity
 | 1 |  | 0 | 1 | High Parity (Sticky)
 | 1 |  | 1 | 1 | Low Parity (Sticky)
Bit 2 | Length of Stop Bit |  |  |  | 
 | 0 |  | One Stop Bit |  | 
 | 1 |  | 2 Stop bits for words of length 6,7 or 8 bits or 1.5 Stop Bits for Word lengths of 5 bits. |  | 
Bits 0 And 1 | Bit 1 |  | Bit 0 | Word Length | 
 | 0 |  | 0 | 5 Bits | 
 | 0 |  | 1 | 6 Bits | 
 | 1 |  | 0 | 7 Bits | 
 | 1 |  | 1 | 8 Bits | 

## Slide 41: MCR: Modem Control Register
Bit | Notes
Bit 7 | Reserved
Bit 6 | Reserved
Bit 5 | Autoflow Control Enabled (16750 only)
Bit 4 | LoopBack Mode
Bit 3 | Aux Output 2
Bit 2 | Aux Output 1
Bit 1 | Force Request to Send
Bit 0 | Force Data Terminal Ready
Notes: The Modem Control Register is a Read/Write Register. Bits 5,6 and 7 are reserved. Bit 4 activates the loopback mode. In Loopback mode the transmitter serial output is placed into marking state. The receiver serial input is disconnected. The transmitter out is looped back to the receiver in. DSR, CTS, RI & DCD are disconnected. DTR, RTS, OUT1 & OUT2 are connected to the modem control inputs. The modem control output pins are then place in an inactive state. In this mode any data which is placed in the transmitter registers for output is received by the receiver circuitry on the same chip and is available at the receiver buffer. This can be used to test the UARTs operation.
Aux Output 2 maybe connected to external circuitry which controls the UART-CPU interrupt process. Aux Output 1 is normally disconnected, but on some cards is used to switch between a 1.8432MHZ crystal to a 4MHZ crystal which is used for MIDI. Bits 0 and 1 simply control their relevant data lines. For example setting bit 1 to '1' makes the request to send line active.

## Slide 42: Modem Status Register
Bit | Notes
Bit 7 | Carrier Detect
Bit 6 | Ring Indicator
Bit 5 | Data Set Ready
Bit 4 | Clear To Send
Bit 3 | Delta Data Carrier Detect
Bit 2 | Trailing Edge Ring Indicator
Bit 1 | Delta Data Set Ready
Bit 0 | Delta Clear to Send

## Slide 43: LSR: Line Status Register
Bit | Notes
Bit 7 | Carrier Detect
Bit 6 | Ring Indicator
Bit 5 | Data Set Ready
Bit 4 | Clear To Send
Bit 3 | Delta Data Carrier Detect
Bit 2 | Trailing Edge Ring Indicator
Bit 1 | Delta Data Set Ready
Bit 0 | Delta Clear to Send

## Slide 44: IER: Interrupt Enable Register
Bit | Notes
Bit 7 | Reserved
Bit 6 | Reserved
Bit 5 | Enables Low Power Mode (16750)
Bit 4 | Enables Sleep Mode (16750)
Bit 3 | Enable Modem Status Interrupt
Bit 2 | Enable Receiver Line Status Interrupt
Bit 1 | Enable Transmitter Holding Register Empty Interrupt
Bit 0 | Enable Received Data Available Interrupt

## Slide 45: IIR: Interrupt Identification Register
Bit | Notes |  | 
Bits 6 and 7 | Bit 6 | Bit 7 | 
 | 0 | 0 | No FIFO
 | 0 | 1 | FIFO Enabled but Unusable
 | 1 | 1 | FIFO Enabled
Bit 5 | 64 Byte Fifo Enabled (16750 only) |  | 
Bit 4 | Reserved |  | 
Bit 3 | 0 | Reserved on 8250, 16450 | 
 | 1 | 16550 Time-out Interrupt Pending | 
Bits 1 and 2 | Bit 2 | Bit 1 | 
 | 0 | 0 | Modem Status Interrupt
 | 0 | 1 | Transmitter Holding Register Empty Interrupt
 | 1 | 0 | Received Data Available Interrupt
 | 1 | 1 | Receiver Line Status Interrupt
Bit 0 | 0 | Interrupt Pending | 
 | 1 | No Interrupt Pending | 
Notes: The interrupt identification register is a read only register. Bits 6 and 7 give status on the FIFO Buffer. When both bits are '0' no FIFO buffers are active. This should be the only result you will get from a 8250 or 16450. If bit 7 is active but bit 6 is not active then the UART has it's buffers enabled but are unusable. This occurs on the 16550 UART where a bug in the FIFO buffer made the FIFO's unusable. If both bits are '1' then the FIFO buffers are enabled and fully operational.
Bits 4 and 5 are reserved. Bit 3 shows the status of the time-out interrupt on a 16550 or higher.
Lets jump to Bit 0 which shows whether an interrupt has occurred. If an interrupt has occurred it's status will shown by bits 1 and 2. These interrupts work on a priority status. The Line Status Interrupt has the highest Priority, followed by the Data Available Interrupt, then the Transmit Register Empty Interrupt and then the Modem Status Interrupt which has the lowest priority.

## Slide 46: Interfacing RS232 to TTL logic levels
RS232

## Slide 47
SPECIFICATIONS |  | RS232 | RS423(not wide use) | RS422 | RS485
Mode of Operation |  | SINGLE -ENDED | SINGLE -ENDED | DIFFERENTIAL | DIFFERENTIAL
Total Number of Drivers and Receivers on One Line (One driver active at a time for RS485 networks) |  | 1 DRIVER 1 RECVR | 1 DRIVER 10 RECVR | 1 DRIVER 10 RECVR | 32 DRIVER 32 RECVR
Maximum Cable Length |  | 50 FT. | 4000 FT. | 4000 FT. | 4000 FT.
Maximum Data Rate (40ft. - 4000ft. for RS422/RS485) |  | 20kb/s | 100kb/s | 10Mb/s-100Kb/s | 10Mb/s-100Kb/s
Maximum Driver Output Voltage |  | +/-25V | +/-6V | -0.25V to +6V | -7V to +12V
Driver Output Signal Level (Loaded Min.) | Loaded | +/-5V to +/-15V | +/-3.6V | +/-2.0V | +/-1.5V
Driver Output Signal Level (Unloaded Max) | Unloaded | +/-25V | +/-6V | +/-6V | +/-6V
Driver Load Impedance (Ohms) |  | 3k to 7k | >=450 | 100 | 54
Max. Driver Current in High Z State | Power On | N/A | N/A | N/A | +/-100uA
Max. Driver Current in High Z State | Power Off | +/-6mA @ +/-2v | +/-100uA | +/-100uA | +/-100uA
Slew Rate (Max.) |  | 30V/uS | Adjustable | N/A | N/A
Receiver Input Voltage Range |  | +/-15V | +/-12V | -10V to +10V | -7V to +12V
Receiver Input Sensitivity |  | +/-3V | +/-200mV | +/-200mV | +/-200mV
Receiver Input Resistance (Ohms), (1 Standard Load for RS485) |  | 3k to 7k | 4k min. | 4k min. | >=12k

## Slide 48: RS 232 Vs RS485
RS232 Limitations
  Speed Distance No of devices
  RS232 20 kbps 50-100 ft 1
  RS485 10Mbps 4000ft 25
  RS232 Dual supply or expensive V convertion
  RS485 Single +5V TTL

## Slide 49: How to get a port USB/RS232 to RS485 converters

## Slide 50: Plug into main bus ISA or PCI

## Slide 51: Full Duplex

## Slide 52: Full duplex multidrop

## Slide 53: Half Duplex